## Slide 1: 6G Upper Midband Technology- Near-field Communication
EEEE.789
Shima Mashhadi
Jan 2025
RIT

## Slide 2
Fresnel region is characterized by the fact that the amplitude variations can be neglected, but not the phase variations.
RIT
Nearfield of the Antenna Array
Example : Fraunhofer distance
0.5×0.5, 3 GHz = 10 m
1×1 m, 15 GHz = 200m
1×1 m, 30 GHz = 400 m
Planar wavefront
Curved wavefront
6G in the Upper Mid-Band: The Rise of Gigantic MIMO - YouTube

## Slide 3
RIT
What is Beamforming ?
d
Considering a simple SIMO
Transmitter in the far-field

## Slide 4
RIT
What is Beam Forming ?
d

## Slide 5
RIT
What is Beam Forming ?
d
What is Beamforming? ("the best explanation I’ve ever heard") - YouTube

## Slide 6
RIT
What is Beam Forming ?
The received signal become M times larger
Achievable in LOS
Receiver
What is Beamforming? ("the best explanation I’ve ever heard") - YouTube

## Slide 7
RIT
What is Beam Forming ?
https://www.oreilly.com/library/view/80211ac-a-survival/9781449357702/ch04.html
Antennas transmit the signal with the phase-shift
Send the radio energy preferentially in one direction
Transmitter
Basics of Antennas and Beamforming - YouTube

## Slide 8
RIT
What is Beam Forming ?

## Slide 9
RIT
What is Beam Forming ?
What is the best thing we can do in the far-field?
Multi-user MIMO (MU-MIMO)

## Slide 10
RIT
Beampattern in the Near-Field
How about the shape of the beam in the Near-field?

## Slide 11
What happens if the user is located in the Fresnel region?
RIT
Near-field Beampatterns

## Slide 12
RIT
Beam Focusing
M = 250
F = 20 m
The gain is the same in the Far-Field and Near-Field

## Slide 13
A uniform squared array with M antenna
RIT
Beam Focusing in the Near-Field
Taylor approximation
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 14
RIT
Beam Focusing in the Near-field
A uniform squared array with M antenna
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 15
RIT
Beam Focusing in the Near-field
A uniform squared array with M antenna
Array Gain
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 16
RIT
Beam Focusing in the Near-field
A uniform squared array with M antenna
Array Gain
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 17
RIT
Beamwidth in the nearfield
Focus point
Array Gain
Focus point
Kosasih A, Demir ÖT, Björnson E. Achieving Beamfocusing via Two Separated Uniform Linear Arrays. arXiv preprint arXiv:2412.03232. 2024 Dec 4.

## Slide 18
RIT
Beamwidth in the nearfield
Focus point
Array Gain
Kosasih A, Demir ÖT, Björnson E. Achieving Beamfocusing via Two Separated Uniform Linear Arrays. arXiv preprint arXiv:2412.03232. 2024 Dec 4.

## Slide 19
RIT
Beamwidth in the Near-field
M = 150
F = 20 m
BW3dB = 0.236 m
M = 250
F = 20 m
BW3dB = 0.141 m
Kosasih A, Demir ÖT, Björnson E. Achieving Beamfocusing via Two Separated Uniform Linear Arrays. arXiv preprint arXiv:2412.03232. 2024 Dec 4.

## Slide 20
RIT
Beamdepth in the Near-field
Array Gain
Focus point
Ramezani P, Björnson E. Near-field beamforming and multiplexing using extremely large aperture arrays. In Fundamentals of 6G Communications and Networking 2023 Jul 10 (pp. 317-349).
F
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 21
RIT
Beamdepth in the Near-field
Array Gain
Ramezani P, Björnson E. Near-field beamforming and multiplexing using extremely large aperture arrays. In Fundamentals of 6G Communications and Networking 2023 Jul 10 (pp. 317-349).
Polk C. Optical Fresnel-zone gain of a rectangular aperture. IRE Transactions on Antennas and Propagation. 1956 Jan;4(1):65-9.
F

## Slide 22
RIT
Beamdepth in the Near-field
Fresnel integrals
F
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 23
RIT
Beamdepth in the Near-field
F
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 24
RIT
Beamdepth in the Near-field
Decreasing function for
Notes: Plot the function in matlab and show the point in the figure

## Slide 25
RIT
Beamdepth in the Near-field
Decreasing function for
Björnson E, Chae CB, Heath Jr RW, Marzetta TL, Mezghani A, Sanguinetti L, Rusek F, Castellanos MR, Jun D, Demir ÖT. Towards 6G MIMO: Massive spatial multiplexing, dense arrays, and interplay between electromagnetics and processing. arXiv preprint arXiv:2401.02844. 2024 Jan 5.

## Slide 26
RIT
Beamdepth in the Near-field

## Slide 27
RIT
Beamdepth in the Near-field
M = 150
F = 20 m
BW = 0.236 m
BD = 39.72m
M = 500
F = 20 m
BW =0.0708m
BD= 3.226m
M = 250
F = 20 m
BW = 0.141 m
BD = 9.26m

## Slide 28
RIT
Nearfield spatial multiplexing
Impact of the wavelength
Fixed array size:
Fixed number of elements:
Far-field
Nearfield

## Slide 29
RIT
Nearfield spatial multiplexing
Smaller focus area in Nearfield, both in depth and width.
Reduce interference between concurrent signal transmission.
Massive spatial multiplexing
Ramezani P, Kosasih A, Irshad A, Björnson E. Exploiting the depth and angular domains for massive near-field spatial multiplexing. IEEE BITS the Information Theory Magazine. 2023 Oct 6;3(1):14-26.

## Slide 30
RIT
Bessel Beam
Headland D, Monnai Y, Abbott D, Fumeaux C, Withayachumnankul W. Tutorial: Terahertz beamforming, from concepts to realizations. Apl Photonics. 2018 May 1;3(5).
A long column of constructive interference can be seen along the z-axis.
As the wave propagates, the beam profile remains invariant.

## Slide 31
RIT
Bessel Beam
Headland D, Monnai Y, Abbott D, Fumeaux C, Withayachumnankul W. Tutorial: Terahertz beamforming, from concepts to realizations. Apl Photonics. 2018 May 1;3(5).

## Slide 32
RIT
Bessel Beam
Bessel beam - Wikipedia
A. Singh et al., "Wavefront Engineering: Realizing Efficient Terahertz Band Communications in 6G and Beyond," in IEEE Wireless Communications, vol. 31, no. 3, pp. 133-139, June 2024.
Bessel beams are self-healing.

## Slide 33
RIT
Curved Beam
Guerboukha H, Zhao B, Fang Z, Knightly E, Mittleman DM. Curving THz Beams in the Near Field: A Framework to Compute Link Budgets. In2024 18th European Conference on Antennas and Propagation (EuCAP) 2024 Mar 17 (pp. 1-5). IEEE.
Trajectory
Result Beam
Solve challenges associated to blockage.
Follow arbitrary curved trajectories​

## Slide 34
RIT
Bessel and Curved Beam

## Slide 35
RIT
Will Near-Field Effects Appear in 6G?
Björnson E, Kara F, Kolomvakis N, Kosasih A, Ramezani P, Salman MB. Enabling 6G performance in the upper mid-band through gigantic MIMO. arXiv preprint arXiv:2407.05630. 2024 Jul.
Example :
0.5×0.5, 3 GHz = 1 m
1×1 m, 15 GHz = 20m
1×1 m, 30 GHz = 40 m
We need extremely large antenna array or very high frequency

## Slide 36: Mini Matlab Project
RIT
ULA1
ULA2

## Slide 37
RIT
National Radio Dynamic Zones (SII-NRDZ)
Allows radio waves to transmit freely.
  Advanced technologies for spectrum sharing and coexistence.
What is the Dynamic Zone?​
Why It Matters
  Spectrum is a limited resource.​
  Traditional methods are insufficient.​
https://www.cs.albany.edu/nrdz-ra/
https://new.nsf.gov/funding/opportunities/sii-nrdz-spectrum-innovation-initiative-national-radio-dynamic-zones/505990/nsf22-579

## Slide 38
Location:
Key Objectives:
RIT
Dynamic Zone in Action: Hat Creek Radio Observatory (HCRO)
RF Baseline Surveys (RFBS)
Exploring Spectrum Sharing Approaches
radio astronomy and satellites
San Francisco, California
https://www.colorado.edu/lab/wirg/research/spectrum-sharing/nsf-sii-nrdz-hcro-nrdz-field-deployment
https://www.youtube.com/watch?v=se9halsveGI
https://lh3.googleusercontent.com/p/AF1QipPoNhQhKOqbjJdZNW2tIXe35B-OqKV74wtsLDQf=s680-w680-h510

## Slide 39
RIT
How to detect aliens' signals?
NASA's Project Cyclops in 1971
Detect signals traveling up to 1000 light-years
Absorbtion
Noise
Distinguishable from natural sources
Microwaves
1 mm – 1 m
https://en.wikipedia.org/wiki/Water_hole_(radio)
https://en.wikipedia.org/wiki/Project_Cyclops
https://www.seti.net/NewToSETINet/aboutSETINet/about.php
https://www.seti.net/indepth/waterhole/waterhole.php

## Slide 40
RIT
Waterhole
There is a magical narrow gate in Microwaves
The 242 MHz area, between the hydrogen line (1420 MHz) and the hydroxyl lines (1662MHz), are the quietest part of the spectrum
Water hole
18cm-21cm
https://en.wikipedia.org/wiki/Water_hole_(radio)
https://en.wikipedia.org/wiki/Project_Cyclops
https://en.wikipedia.org/wiki/Hydroxyl_radical
https://en.wikipedia.org/wiki/Hydrogen_line

## Slide 41
RIT
Waterhole
1420-1662 MHz
Oliver:
“What more poetic place could there be for water-based life to seek its kind than the age-old meeting place for all species: the water hole”
Waterhole
18cm-21cm
https://www.seti.net/indepth/waterhole/waterhole.php