## Slide 1: 6G Midband Technology and Spectrum
Shima Mashhadi
Jan 2025
RIT

## Slide 2
RIT
Current allocations and uses in 7.125 - 24 GHz in the U.S.
7.125 - 24 GHz band is split into four sub-categories for ease of presentation and analysis
8.5-13.75 GHz
7.125 - 8.5 GHz
13.75-17.1 GHz
17.1 - 24 GHz

## Slide 3
RIT
 | 7125 | 7145 | 7190 | 7235 | 7250 | 7300 | 7375 | 7450 | 7550 | 7750 | 7900 | 8025 | 8175 | 8215 | 8400 | 8450
F | Fixed (FS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
F |  |  | Earth Exploration Satellite(EESS) |  |  |  | Mobile(MS) |  |  |  |  | Earth Exploration Satellite(EESS) |  |  |  | 
N |  |  |  |  |  |  |  |  |  |  |  | EESS |  |  |  | 
F |  |  |  |  | Fixed satellite (FSS) |  |  |  |  |  | Fixed satellite (FSS) |  |  |  |  | 
F |  |  | MetSat |  |  |  |  | MetSat |  | MetSat |  | MetSat |  |  |  | 
F |  |  |  |  | Mobile-Satellite (MSS) |  |  |  |  |  | Mobile-Satellite (MSS) |  |  |  |  | 
F |  | Space Research (SRS) |  |  |  |  | Maritime Mobile Satellite (MMSS) |  |  |  |  |  |  |  | Space Research (SRS) | 
N |  | SRS |  |  |  |  |  |  |  |  |  |  |  |  | SRS | 
7.125 - 8.5 GHz
FS, FSS and MSS are the largest current allocations
Approximately 20% of FS use is by the Department of Defense (DoD),
The 8400 – 8500 MHz band is allocated for SRS (DL).
Other uses may not be ubiquitous and hence perhaps more amenable to sharing.

## Slide 4
RIT
 | 7125 | 7145 | 7190 | 7235 | 7250 | 7300 | 7375 | 7450 | 7550 | 7750 | 7900 | 8025 | 8175 | 8215 | 8400 | 8450
F | Fixed (FS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
F |  |  | Earth Exploration Satellite(EESS) |  |  |  | Mobile(MS) |  |  |  |  | Earth Exploration Satellite(EESS) |  |  |  | 
N |  |  |  |  |  |  |  |  |  |  |  | EESS |  |  |  | 
F |  |  |  |  | Fixed satellite (FSS) |  |  |  |  |  | Fixed satellite (FSS) |  |  |  |  | 
F |  |  | MetSat |  |  |  |  | MetSat |  | MetSat |  | MetSat |  |  |  | 
F |  |  |  |  | Mobile-Satellite (MSS) |  |  |  |  |  | Mobile-Satellite (MSS) |  |  |  |  | 
F |  | Space Research (SRS) |  |  |  |  | Maritime Mobile Satellite (MMSS) |  |  |  |  |  |  |  | Space Research (SRS) | 
N |  | SRS |  |  |  |  |  |  |  |  |  |  |  |  | SRS | 
7.125 - 8.5 GHz
6G

## Slide 5
RIT
 | 8.5 |  | 8.65 |  | 8.85 |  | 9.2 |  | 9.5 |  | 9.9 |  | 10 |  | 10.4 |  | 10.5 |  | 10.6 |  | 10.7 |  | 11.2 |  | 11.7 |  | 12.1 |  | 12.5 |  | 12.75 |  | 13.4 | 
N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | FS |  |  | Fixed (FS) |  |  |  |  |  |  | Fixed (FS) |  |  |  |  |  | 
N |  |  |  |  |  |  |  | EESS |  |  |  |  |  |  |  |  |  |  | EESS |  |  |  |  |  |  |  |  | BSS |  | Mobile(MS) |  | EESS |  | 
 | Radiolocation (RLS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | FSS |  |  |  |  |  |  |  |  | FSS |  |  |  | 
 |  |  |  |  |  |  |  | SRS |  |  | MetSat |  |  |  |  |  |  |  | SRS |  |  |  |  |  |  |  |  |  |  |  |  | SRS |  | 
 |  |  |  | AR |  | AR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | AR |  | 
8.5-13.75 GHz
RLS is the single largest allocation.
~2500 MHz in 10.7 – 13.25 GHz is allocated for non-federal use, of which 12.2 - 13.25 GHz is already under consideration by the FCC for sharing with other services.
13.25 - 13.75 may also be available for sharing with limited restrictions.
(RAS)
RLS

## Slide 6
RIT
 | 8.5 |  | 8.65 |  | 8.85 |  | 9.2 |  | 9.5 |  | 9.9 |  | 10 |  | 10.4 |  | 10.5 |  | 10.6 |  | 10.7 |  | 11.2 |  | 11.7 |  | 12.1 |  | 12.5 |  | 12.75 |  | 13.4 | 
N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | FS |  |  | Fixed (FS) |  |  |  |  |  |  | Fixed (FS) |  |  |  |  |  | 
N |  |  |  |  |  |  |  | EESS |  |  |  |  |  |  |  |  |  |  | EESS |  |  |  |  |  |  |  |  | BSS |  | Mobile(MS) |  | EESS |  | 
 | Radiolocation (RLS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | FSS |  |  |  |  |  |  |  |  | FSS |  |  |  | 
 |  |  |  |  |  |  |  | SRS |  |  | MetSat |  |  |  |  |  |  |  | SRS |  |  |  |  |  |  |  |  |  |  |  |  | SRS |  | 
 |  |  |  | AR |  | AR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | AR |  | 
8.5-1375 GHz
Passive EESS in the nearby 10.6−10.7 GHz band
(RAS)

## Slide 7
RIT
 | 13.75 | 14 | 14.2 | 14.3 | 14.4 | 14.47 | 14.5 | 14.71 | 14.75 | 14.8 | 15.13 | 15.35 | 15.4 | 15.43 | 15.63 | 15.7 | 16.6
 |  |  |  |  | Fixed (FS) |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | Mobile(MS) |  |  |  |  |  |  |  |  |  |  |  | 
F |  |  |  |  |  |  |  |  |  |  | EESS | EESS |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | RAS |  |  |  |  | 
 | RLS |  |  |  |  |  |  |  |  |  |  |  | Radiolocation (RLS) |  |  |  | 
 |  |  |  |  |  |  | Space Researc (SRS) |  |  |  |  |  | Aeronautical Radionavigation (AR) |  |  |  | SRS
 |  | Mobile-Satelite (MSS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Fixed Satellite (FSS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13.75-17.1 GHz
RLS, SRS, FS and MS are the largest allocations in this part of the spectrum.
200 MHz between 14.2 – 14.4 GHz is not allocated for federal use.

## Slide 8
RIT
 | 13.75 | 14 | 14.2 | 14.3 | 14.4 | 14.47 | 14.5 | 14.71 | 14.75 | 14.8 | 15.13 | 15.35 | 15.4 | 15.43 | 15.63 | 15.7 | 16.6
 |  |  |  |  | Fixed (FS) |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | Mobile(MS) |  |  |  |  |  |  |  |  |  |  |  | 
F |  |  |  |  |  |  |  |  |  |  | EESS | EESS |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | RAS |  |  |  |  | 
 | RLS |  |  |  |  |  |  |  |  |  |  |  | Radiolocation (RLS) |  |  |  | 
 |  |  |  |  |  |  | Space Researc (SRS) |  |  |  |  |  | Aeronatical Radionavigation (AR) |  |  |  | SRS
 |  | Mobile-Satelite (MSS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Fixed Satellite (FSS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13.75-17.1 GHz
6G

## Slide 9
RIT
 | 17.1 |  | 17.3 |  | 17.8 |  | 18.1 |  | 18.4 |  | 18.8 |  | 19.7 |  | 20.2 |  | 21.4 |  | 22.21 |  | 22.55 |  | 23.55 | 
 |  |  |  |  |  |  |  | Fixed (FS) |  |  |  |  |  |  | MSS | Fixed (FS) |  |  |  |  |  |  |  | 
 |  |  |  | Fixed (FS) |  |  |  |  |  |  |  |  | MSS |  |  | Fixed (FS) |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Mobile(MS) |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | RAS | RAS |  | RAS |  |  | RAS
 | RLS |  |  |  | MetSat |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ISS |  |  | 
 |  | SRS |  |  |  |  |  |  |  | SRS |  |  |  |  |  | SRS |  |  | SRS |  | SRS |  |  | SRS
 |  | EESS |  |  |  |  |  |  |  | EESS |  |  |  |  |  | EESS |  |  | EESS |  |  |  |  | EESS
 |  |  | FSS |  | Fixed Satellite (FSS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Fixed Satellite (FSS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
17.1-24 GHz
100 MHz spectrum in 17.7 – 17.8 GHz is not allocated for federal use.
2,200 MHz of spectrum in 17.8 – 18.6 GHz and 18.8 – 20.2 GHz may be practical for coexistence if used for earth stations rather than user devices.
Notes: Sharing Spectrum and Services in the 7-24 GHz Upper Midband
18.8 − 20.2 GHz: While the propagation characteristics of this band are less favorable than the lower ones, hotspots and Wireless Local Area Network (WLAN) can benefit of the higher bandwidth, comparable to the ones available at the higher mmWave frequencies, while maintaining good coverage (above 80%),
NON Federal : 18.4-18.6 SRS and EESS are passive
NSF 17.8-19.7 Radio asstoronomy research
FEderal FSS the DL of som satellite network
18.6-18.8NASA passive sensing of the Earth from the space rain rates Sea State, sea ice, ocean wind speed and humidity.

## Slide 10
RIT
Potential Shared Spectrum Bands
7.125-8.5 GHz
Federal Fixed
Federal Fixed satellite
10.7-13.25 GHz
Non-Federal Satellite Services
14.0-14.2 GHz
17.8-18.6 GHz and 18.8-20.2 GHz
Federal Satellite
Additional analysis need to be done with regard to commercial satellite
Federal Mobile Satellite
Space Research

## Slide 11
RIT
Fundamental sharing framework
Success of spectrum sharing depends upon a few basic components:
New entrant capabilities
Incumbent capabilities and limitations
Frequency and time coordination capabilities
Interference reporting mechanisms
They have to work in harmony with each other for the overall benefit

## Slide 12
RIT
6G Spectrum
6G demand : Peak data rate 200 Gbit/s
More Bandwidth?
5G
6G
Upper Mid
WRC-23 candidates:
4.4-4.8 GHz (400 MHz)
7.1-8.4 GHz (600-1275 MHz)
14.8-15.35 GHz (550 MHz)
Current 5G candidates:
3.3-3.8 GHz (400 MHz)
6.4-7.1 GHz (700 MHz)
6G will only have slightly more bandwidth than 5G
Björnson E, Kara F, Kolomvakis N, Kosasih A, Ramezani P, Salman MB. Enabling 6G performance in the upper mid-band through gigantic MIMO. arXiv preprint arXiv:2407.05630. 2024 Jul.
Notes: https://www.youtube.com/watch?v=TJK1PvfAgQU
https://www.youtube.com/watch?v=70BOKA0PmdE

## Slide 13
RIT
6G Spectrum
More Bandwidth?
Bigger MIMO
6G will only have slightly more bandwidth than 5G
5G
100 MHz
6G
200-400 MHz
64 Antenna
2x-4x
128 – 256 Antenna
Björnson E, Kara F, Kolomvakis N, Kosasih A, Ramezani P, Salman MB. Enabling 6G performance in the upper mid-band through gigantic MIMO. arXiv preprint arXiv:2407.05630. 2024 Jul. https://www.academia.edu/download/118233219/2407.05630.pdf
Notes: https://www.youtube.com/watch?v=TJK1PvfAgQU
https://www.youtube.com/watch?v=70BOKA0PmdE

## Slide 14
RIT
The need for 6G
6G demand : Peak data rate 200 Gbit/s
Increase the Frequency and number of the antenna
Bigger MIMO
More Bandwidth?
6G will only have slightly more bandwidth than 5G
Notes: https://www.youtube.com/watch?v=TJK1PvfAgQU
https://www.youtube.com/watch?v=70BOKA0PmdE

## Slide 15
Friis' formula: the received power from an isotropic transmitter antenna
RIT
What Happens to Path Loss at High Frequencies?
Higher frequency Less power
Björnson E, Sanguinetti L. Power scaling laws and near-field behaviors of massive MIMO and intelligent reflecting surfaces. IEEE Open Journal of the Communications Society. 2020 Sep 1;1:1306-24.

## Slide 16
RIT
What Happens to Path Loss at High Frequencies?
A reasonable design goal is to keep the free-space path-loss constant when frequency increased
d
Received power with array areas At and Ar
Higher frequency More power!!
We need more antenna to fill the area
Björnson E, Kara F, Kolomvakis N, Kosasih A, Ramezani P, Salman MB. Enabling 6G performance in the upper mid-band through gigantic MIMO. arXiv preprint arXiv:2407.05630. 2024 Jul.
6G in the Upper Mid-Band: The Rise of Gigantic MIMO - YouTube

## Slide 17
RIT
What happen to pathloss in high frequency?
d
Higher frequency More power!!
Improve the free space pathloss by increasing the number of the antenna but the same aperture area
So what is the problem with mmWave?
6G in the Upper Mid-Band: The Rise of Gigantic MIMO - YouTube

## Slide 18
Just more links between the transmitter and receiver?
Just a bigger channel matrix?
Just more complexity?
RIT
What happen if we increase the number of the antennas?

## Slide 19
Just more links between the transmitter and receiver?
Just a bigger channel matrix?
Just more complexity?
RIT
What happen if we increase the number of the antennas?
Nearfield Communication

## Slide 20
Considering a simple SIMO channel with LOS
RIT
SIMO Channel Model
r
Aperture Antenna D
d

## Slide 21
Considering a simple SIMO channel with LOS
RIT
SIMO Channel Model in Near-field
r
Aperture Antenna D
Taylor approximation
Wang Z, Mu X, Liu Y. Near-field integrated sensing and communications. IEEE Communications Letters. 2023 May 25;27(8):2048-52.

## Slide 22
RIT
r
Aperture Antenna D
For the enough large r (far-field) equal to 0
SIMO Channel Model in Near-field

## Slide 23
RIT
r
Aperture Antenna D
For the enough large r (far-field) equal to 0
But how much large?
SIMO Channel Model in Nearfield

## Slide 24
RIT
Phase Variation in the Nearfield of the Antenna Array
What is the largest phase shift for a given r?
r
r
Fraunhofer array distance
Taylor approximation
Björnson E, Demir ÖT, Sanguinetti L. A primer on near-field beamforming for arrays and reconfigurable intelligent surfaces. In2021 55th Asilomar Conference on Signals, Systems, and Computers 2021 Oct 31 (pp. 105-112). IEEE.

## Slide 25
RIT
Phase Variation in the Nearfield of the Antenna Array
Fraunhofer array distance
Curved wavefront
Far-field
phase variation depends on the incident angle.
Planar wavefront
phase variation depends on the incident angle and distance.
Nearfield

## Slide 26
The spherical curvature also gives rise to power variations over the receive antenna.
RIT
Power Variation in Nearfield of the Antenna Array
The power differences
Bjönson distance
Phase variations are more prevalent
Björnson E, Demir ÖT, Sanguinetti L. A primer on near-field beamforming for arrays and reconfigurable intelligent surfaces. In2021 55th Asilomar Conference on Signals, Systems, and Computers 2021 Oct 31 (pp. 105-112). IEEE.

## Slide 27
Fresnel region and is characterized by the fact that the amplitude variations can be neglected, but not the phase variations.
RIT
Nearfield of the Antenna Array
Example : Fraunhofer distance
0.5×0.5, 3 GHz = 10 m
1×1 m, 15 GHz = 200m
1×1 m, 30 GHz = 400 m
6G in the Upper Mid-Band: The Rise of Gigantic MIMO - YouTube

## Slide 28
RIT
National Radio Dynamic Zones (SII-NRDZ)
Allows radio waves to transmit freely.
  Advanced technologies for spectrum sharing and coexistence.
What is the Dynamic Zone?​
Why It Matters
  Spectrum is a limited resource.​
  Traditional methods are insufficient.​
https://www.cs.albany.edu/nrdz-ra/
https://new.nsf.gov/funding/opportunities/sii-nrdz-spectrum-innovation-initiative-national-radio-dynamic-zones/505990/nsf22-579

## Slide 29
RIT
How to detect aliens' signals?
NASA's Project Cyclops in 1971
Detect signals traveling up to 1000 light-years
Absorbtion
Noise
Distinguishable from natural sources
Microwaves
1 mm – 1 m
https://en.wikipedia.org/wiki/Water_hole_(radio)
https://en.wikipedia.org/wiki/Project_Cyclops
Notes: He went on to list the following reasons:
Galactic noise (synchrotron radiation) at a minimum
Thermal noise (receiver and isotropic background noise) at a minimum
Quantum noise (spontaneous emissions or shot noise) at low level
Star noise at a low level
https://www.seti.net/NewToSETINet/aboutSETINet/about.php
https://www.seti.net/indepth/waterhole/waterhole.php

## Slide 30
RIT
Waterhole
There is a magical narrow gate in Microwaves
The 242 MHz area, between the hydrogen line (1420 MHz) and the hydroxyl lines (1662MHz), are the quietest part of the spectrum
Water hole
18cm-21cm
https://en.wikipedia.org/wiki/Water_hole_(radio)
https://en.wikipedia.org/wiki/Project_Cyclops
https://en.wikipedia.org/wiki/Hydroxyl_radical
https://en.wikipedia.org/wiki/Hydrogen_line

## Slide 31
RIT
Waterhole
1420-1662 MHz
Oliver:
“What more poetic place could there be for water-based life to seek its kind than the age-old meeting place for all species: the water hole”
Waterhole
18cm-21cm
https://www.seti.net/indepth/waterhole/waterhole.php